## Slide 1: Detection Limits Demystified
Craig Hutchings
October 2015

## Slide 2: Why Are Detection Limits Important

## Slide 3: Detection Limits Affect Data Interpretation
Chart: Concentration (ug/kg)
| N0 | N1 | N2 | N3 | N4 | AY | AE | B | DF | F0 | F1 | F2 | F3 | A0 | P0 | PA1 | PA2 | PA3 | PA4 | DBT0 | DBT1 | DBT2 | DBT3 | FL0 | PY0 | FP1 | BA0 | C0 | BC1 | BC2 | BC3 | BC4 | BBF | BKF | BEP | BAP | PER | DA | IND | GHI | HOP
DL 10 | 12 | 19 | 23 | 18 | 11
DL 5 | 5.1 | 5.3 | 7 | 6.5 | 5.3 | 8.5 | 9.5 | 8.2 | 6 | 5.1 | 5.9 | 5.6 | 6
DL1 | 1.4 | 2.1 | 4.8 | 0 | 2 | 3 | 0 | 2 | 3 | 4 | 3 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 4: Nondetects May Lurk in Data Set

## Slide 5: Terminology Can Be Confusing
Detected
  MDL
  LOD
  SDL
  EDL
  IDL
Other
  EMPC
Measured
  MRL
  RL
  CRDL
  CRQL
  PQL
  LLQ
  QL
  LOQ

## Slide 6: What is the detection limit for PCBs?
Aroclors or congeners?
Water, sediment, tissue, something else?
Is the site contaminated or pristine?
What will the data be used for?
  Waste disposal
  Screening
  Regulatory review
  Risk assessment

## Slide 7: What Affects Detection Limits
Sample size
Concentration of other constituents
Sample clean-up
Methodology
Lab performance
  Experience
  Extraction technique
  Instrument type and maintenance

## Slide 8: Method Detection Limit - MDL
Statistically determined
The minimum concentration that can be measured with 99% confidence that the concentration is greater than zero
Concentrations near MDL are estimates
Laboratory, instrument, matrix, method, & analyte specific

## Slide 9: MDL continued
Concentrations at MDL expected to be a false positive 1% of the time, but false negatives 50% of the time

## Slide 10: Method Reporting Limit - MRL
May also be referred to as QL (quantitation limit), sample quantitation limit, or just RL (reporting limit)
Determined by the lowest point of the calibration
Not as specific as MDL, labs can adust
Concentrations at MRL can be reliably quantified
MRL > MDL
Also laboratory, instrument, matrix, method, & analyte specific

## Slide 11: Relationship of MDL to MRL
Increasing Concentration
Method Reporting Limit
Method Detection Limit
Notes: Add slide about calibrations

## Slide 12: Other Types of Detection Limits
PQL – Multiple definitions
  Considered to be lowest concentration that can be reliably quantified by a method
For DOD work you may see
    Limit of Detection (LOD) - Lowest concentration that can be detected with a 1% false negative rate.
      Generally 2x to 3X MDL
    Limit of Quantitation (LOQ) – similar to MRL

## Slide 13: Other Types of Detection Limits
Estimated Quantitation Limit (EQL)
  Estimated Detection Limit (EDL)
  Sample Detection Limit (SDL)
PCDD/F specific, but frequently applied to PCB congeners, PBDEs, etc.
2.5 times signal to noise

## Slide 14: EMPC
Estimated Maximum Possible Concentration (EMPC)
Peak present but not all of the identification criteria is met
Always greater than MDL, may be greater than MRL
Generally treated a non-detect in TEQ calculations
EMPCs can present data management difficulties and need to be reviewed in QC checks

## Slide 15: Which Limit Should You Use?
MDL ?
½ MDL ?
MRL ?
Project specific
Consult with regulators

## Slide 16: Questions?